## Slide 1
Pack Line
Electrical Training Course
8 Hour Course – 1 Day

## Slide 2
Introductions
Instructor: Bill Flatley

## Slide 3
Safety Test and Review

## Slide 4
System Safety
(At the Machine)

## Slide 5
Battery Safety Overview
Assembly line personnel must comply with all safety rules.

## Slide 6
Health & Safety
Statement

## Slide 7
General Safety Guidelines
Read the Entire Manual
Good Work Habits
Consider Personal Health
Dress Properly
Clean and Safe Work Area
Safety Signage
ECPL Placard Locations
Use Tools Properly
Electrical System Safety
Mechanical System Safety
Operating Safety Precautions
Safety Devices

## Slide 8
Personal Safety
Accidents often do not occur as the result of a single cause, but may occur because of an
interaction between working conditions, human error, and other events.
Knowledge First
Work Habits
Fitness for Duty
Dressing for Safety
Eye Protection
Hearing Protection
Head Protection
Foot Protection

## Slide 9
Work Area Safety
Cleanliness
Warning Signs
Traffic Areas
Unsafe Conditions
Cell Guarding
Automated Guide Cart (AGC) Safety
Lift Assist Safety
Working at Heights Safety

## Slide 10
ECPL Placards & Tags
Energy Control and Power Lockout

## Slide 11
Tool Usage

## Slide 12
Machine Safety
Electrical Safety
Pneumatic Safety
Mechanical Safety

## Slide 13
Safety Device
Locations

## Slide 14
Safety Device Locations
for Cell EP020 and EP720

## Slide 15
Safety Device Locations
for Cell EP040, EP060, EP080 and EP090

## Slide 16
Safety Device Locations
for Cell EP100 and EP125

## Slide 17
Safety Device Locations
for Cell EP160, EP180, EP200 and EP220

## Slide 18
Safety Device Locations
for Cell EP230 and EP235

## Slide 19
Safety Device Locations
for Cell EP240, EP260 and EP270

## Slide 20
Safety Device Locations
for Cell EP300, EP320 and EP325

## Slide 21
Safety Device Locations
for Cell EP340

## Slide 22
Safety Device Locations
for Cell EP380, EP400 and EP420

## Slide 23
Safety Device Locations
for Cell EP480 and EP485

## Slide 24
Safety Device Locations
for Cell EP500, EP520, EP540 and EP560

## Slide 25
Safety Device Locations
for Cell EP600 and EP610

## Slide 26
Safety Device Locations
for Cell EP620, EP630, EP640 and EP650

## Slide 27
Safety Device Locations
for Cell EP680 and EP700

## Slide 28
Safety Device Locations
for Cell EP905

## Slide 29
Safety Device Locations
for Cell EP020 and EP720

## Slide 30
Energy Control Devices

## Slide 31
Cell Power Distribution Panel

## Slide 32
Cell Main Pneumatic Disconnect
Each cell requires compressed air and has its own air processing equipment that
processes air supplied from the plant and distributes the processed air to the cell
equipment.

## Slide 33
SDS References

## Slide 34
Break

## Slide 35
System
Description Overview
(At the Machine)

## Slide 36
BET/BEV3 Pack Main LineSummary
The BET/BEV3 Pack Main Line is part of a larger BET/BEV3 Battery Pack Assembly System.

## Slide 37
The following lists the 19 battery assembly types handled by the Battery Pack Tests and
Cover Leak Test.

## Slide 38
BET/BEV2 Battery Pack
Assembly System Layouts

## Slide 39
Battery Pack Test System Layout

## Slide 40
Cover Leak Test System Layout

## Slide 41
BET/BEV2 Battery Pack Test
and Cover Leak Test
Utilities

## Slide 42
Battery Pack Test and
Cover Leak Test Utilities – Automated Stations

## Slide 43
Battery Pack Test and
Cover Leak Test Utilities – Manual Stations

## Slide 44
BET/BEV2 Battery Pack Test
and Cover Leak Test
Equipment

## Slide 45
Equipment Matrix – Automated Stations

## Slide 46
Equipment Matrix – Manual Stations

## Slide 47
Station Descriptions and Sequence of Operations

## Slide 48
Common Equipment

## Slide 49
Common Equipment

## Slide 50
Air Preparation Unit

## Slide 51
ArmorStart Controller

## Slide 52
Barcode Reader

## Slide 53
Conveyor Electrical Disconnect

## Slide 54
Cycle Start Button

## Slide 55
Entrance Gate Box

## Slide 56
Nutrunner Controller

## Slide 57
Operator Push Button Box

## Slide 58
Power Distribution Panel

## Slide 59
Safety Device Junction Box

## Slide 60
RTV Dispense System Controller

## Slide 61
RTV Dispense Pump Control Panel

## Slide 62
Bauer Test Computer

## Slide 63
Cell EP680 (1 of 2)

## Slide 64
Cell EP680 (2 of 2)

## Slide 65
Operator Interface Devices

## Slide 66
Controls and Indicators

## Slide 67
Operator Console Human Machine Interface (HMI)

## Slide 68
Operator Emergency Stop (E-Stop)

## Slide 69
Operator Push Button Box
Button | Description
RESPONDER CALL | Call a Team Lead.
MAINTENANCE CALL | Call Maintenance Personnel.
PRINT LABEL | Reprint a label if the original printed label is damaged.
RETEST | NOT USED.

## Slide 70
Cell Power Distribution Panel

## Slide 71
Stack Light
Indicator | Action | Description
Horn | Multiple Beeps | Notification Alert
Horn | One Beep | Scan Passed
Blue | Flashing | Operator Load Prompt
Blue | Fast Flashing | N/A
Blue | Solid | In Cycle
White | Flashing | Flexnet Gate Check Query in Progress
White | Fast Flashing | Flexnet Gate Check Failed
White | Solid | Flexnet Gate Check Passed
Red | Flashing | N/A
Red | Fast Flashing | Maintenance Call
Red | Solid | Station Faulted
Yellow | Flashing | Over Cycle
Yellow | Fast Flashing | Responder Call
Yellow | Solid | Approaching End of Cycle
Green | Flashing | Ready for Cycle
Green | Fast Flashing | N/A
Green | Solid | Process Complete

## Slide 72
Status Beacon
Indicator | Action | Description
Red | Flashing | Maintenance (High Priority Fault) Alarm Present
Red | Solid | Non-Maintenance (Low Priority Fault) Alarm Present

## Slide 73
HMI Screens

## Slide 74
HMI Screen Navigation Paths

## Slide 75
Screen Header

## Slide 76
Select Screen

## Slide 77
Mode Screen

## Slide 78
Service Screen

## Slide 79
Cell Overview Screen

## Slide 80
Cell Power and I/O Screen

## Slide 81
EtherNet Screen

## Slide 82
Alarm Screen

## Slide 83
Maintenance History Screen

## Slide 84
Throughput Overview Screen

## Slide 85
Station Throughput Screen

## Slide 86
Scroll List Screen

## Slide 87
Station Overview Screen

## Slide 88
Robot Screen

## Slide 89
Barcode Screen

## Slide 90
Printer Screen

## Slide 91
Bowl Feeder Screen

## Slide 92
Device Diagnostic Screen

## Slide 93
Configuration Screen

## Slide 94
Operator Function Screen

## Slide 95
Signature Screen

## Slide 96
Camera Screen

## Slide 97
Manual Repair Screen

## Slide 98
Part Present Screen

## Slide 99
Schedule Screen

## Slide 100
Style Overview Screen

## Slide 101
Common Operating Procedures

## Slide 102
Inspecting the Line
Starting Cell in Manual Mode
Starting an Automated Cell
Stopping a Cycle
Cycle Stop
Emergency Stop

## Slide 103
Shutting Down
Recovering from a Fault
Recovering from an Emergency Stop
Recovering from a Fault
Opening and Closing an Entrance Gate

## Slide 104
Modes of Operation

## Slide 105
Hands On
(At the Machine)

## Slide 106
HMI Screens

## Slide 107
Common Operating Procedures

## Slide 108
Modes of Operation

## Slide 109
Manual Station
Operation

## Slide 110
Automated Station
Operation – Auto Mode

## Slide 111
Automated Station
Operation – Manual Mode

## Slide 112
Questions & Answers

## Slide 113
Electrical Drawings
Overview

## Slide 114
TIS and TIV
Overview

## Slide 115
Questions & Answers

## Slide 116
TIS and TIV Overview
(At the Machine)

## Slide 117
Questions & Answers

## Slide 118
Troubleshooting
and Faults
(At the Machine)

## Slide 119
Questions & Answers

## Slide 120
Class Wrap-Up
Closing Remarks
Complete Task Certifications
Complete Course Evaluations