## Slide 1
Battery Pack Test & Cover Leak Test & Pack Line
EP280 & EP580 & EP680
Operator Training Course
4 Hour Course – ½ Day

## Slide 2
Introductions
Instructor: Bill Flatley

## Slide 3
Safety Test and Review

## Slide 4
System Safety
(At the Machine)

## Slide 5
Battery Safety Overview
Assembly line personnel must comply with all safety rules.

## Slide 6
Health & Safety
Statement

## Slide 7
General Safety Guidelines
Read the Entire Manual
Good Work Habits
Consider Personal Health
Dress Properly
Clean and Safe Work Area
Safety Signage
ECPL Placard Locations
Use Tools Properly
Electrical System Safety
Mechanical System Safety
Operating Safety Precautions
Safety Devices

## Slide 8
Personal Safety
Accidents often do not occur as the result of a single cause, but may occur because of an
interaction between working conditions, human error, and other events.
Knowledge First
Work Habits
Fitness for Duty
Dressing for Safety
Eye Protection
Hearing Protection
Head Protection
Foot Protection

## Slide 9
Work Area Safety
Cleanliness
Warning Signs
Traffic Areas
Unsafe Conditions
Cell Guarding
Automated Guide Cart (AGC) Safety

## Slide 10
ECPL Placards & Tags
Energy Control and Power Lockout

## Slide 11
Tool Usage

## Slide 12
Machine Safety
Electrical Safety
Pneumatic Safety
Mechanical Safety

## Slide 13
Safety Device
Locations

## Slide 14
Safety Device Locations
for Cell EP280 and EP580 - Mezzanine

## Slide 15
Safety Device Locations
for Cell EP280 and EP580 – Under Mezzanine

## Slide 16
Safety Device Locations
for Cell EP680

## Slide 17
Energy Control Devices

## Slide 18
Cell Power Distribution Panel

## Slide 19
Cell Main Pneumatic Disconnect
Each cell requires compressed air and has its own air processing equipment that
processes air supplied from the plant and distributes the processed air to the cell
equipment.

## Slide 20
SDS References

## Slide 21
Break

## Slide 22
System
Description Overview
(At the Machine)

## Slide 23
BET/BEV3 Battery Pack Test
and Cover Leak Test Summary
The BET/BEV3 Batter Pack Tests and Cover Leak Test are part of the Pack Main Line that
is part of a larger BET/BEV3 Battery Pack Assembly System.

## Slide 24
The following lists the 13 battery assembly types handled by the Battery Pack Tests and
Cover Leak Test.
Pack Type | Assembly Type | Modules Per Assembly | Layers
BET | 24 Module Long Wheelbase Off-road | 24 | 2
BET | 24 Module Long Wheelbase | 24 | 2
BET | 20 Module Long Wheelbase Off-road | 20 | 2
BET | 20 Module Long Wheelbase | 20 | 2
BET | 16 Module Long Wheelbase | 16 | 2
BET | 10 Module Long Wheelbase | 10 | 2
BET | 20 Module Short Wheelbase Off-road | 20 | 2
BET | 20 Module Short Wheelbase | 20 | 2
BET | 16 Module Short Wheelbase | 16 | 2
BET | 12 Module Short Wheelbase | 12 | 2
BEV3 | 12 Module Rear Wheel Drive | 12 | 1
BEV3 | 12 Module All Wheel Drive | 12 | 1
BEV3 | 10 Module Rear Wheel Drive | 10 | 1

## Slide 25
BET/BEV2 Battery Pack Test
and Cover Leak Test
System Layouts

## Slide 26
Battery Pack Test System Layout

## Slide 27
Cover Leak Test System Layout

## Slide 28
BET/BEV2 Battery Pack Test
and Cover Leak Test
Utilities

## Slide 29
Battery Pack Test and
Cover Leak Test Utilities – Manual Stations

## Slide 30
BET/BEV2 Battery Pack Test
and Cover Leak Test
Equipment

## Slide 31
Equipment Matrix – Manual Stations

## Slide 32
Common Equipment

## Slide 33
Air Preparation Unit

## Slide 34
Automated Guided Cart (AGC)

## Slide 35
Barcode Reader

## Slide 36
Bypass/Release Toggle Switch

## Slide 37
Cycle Start Button

## Slide 38
Label Printer

## Slide 39
Electrical and Coolant Leak
Test Station EP280 and EP580
Equipment

## Slide 40
Cell EP280 and EP580 – Mezzanine (1 of 3)
TOP VIEW

## Slide 41
Cell EP280 and EP580 – Mezzanine (2 of 3)
TOP VIEW

## Slide 42
Cell EP280 and EP580 – Mezzanine (3 of 3)
TOP VIEW

## Slide 43
Cell EP280 and EP580 – Under Mezzanine
TOP VIEW

## Slide 44
Cell EP280 & EP580
Sequence of Operations

## Slide 45
Leak Test Cart
The Leak Test Cart pressurizes the batter pack coolant circuit and determines if it is leak
Tight using a differential pressure decay test method.

## Slide 46
Bauer Test Computer

## Slide 47
FLIR Thermal Camera
The FLIR Thermal Cameras detect heat.

## Slide 48
Load Cycler
The Cell Load Cycler charges and discharges the Battery Pack for the electrical test
and is controlled by the Baur Test Computer.

## Slide 49
Tool Balancer - Small
The Tool Balancer is an adjustable cable system suspended from the cell frame that allows
tools to hang within reach of the Operator.

## Slide 50
BEV3 X1 LV Connector

## Slide 51
BET Ground Connector 2
BET / BEV3 Ground Connector 1

## Slide 52
BEV3 Outlet Coolant Connector
BET Outlet / BEV3 Inlet Coolant Connector
BET Inlet Coolant Connector

## Slide 53
BET Heater Connector & BET ACEC Connector

## Slide 54
Tool Balancer - Medium
The Tool Balancer is an adjustable cable system suspended from the cell frame that allows
tools to hang within reach of the Operator.

## Slide 55
BET X8 LV Connector & BET X9 LV Connector

## Slide 56
Tool Balancer - Large
The Tool Balancer is an adjustable cable system suspended from the cell frame that allows
tools to hang within reach of the Operator.

## Slide 57
BEV3 DCFC Connector

## Slide 58
BET FPIM / BEV3 IPE Connector

## Slide 59
BET LPIM Connector

## Slide 60
BET RPIM Connector

## Slide 61
BET DCFC Connector

## Slide 62
BET IPE / BEV3 RDU Connector

## Slide 63
Cover Leak Test Station
EP680 Equipment

## Slide 64
Cell EP680 (1 of 2)

## Slide 65
Cell EP680 (2 of 2)

## Slide 66
Cell EP680
Sequence of Operations

## Slide 67
EP680 Bauer Leak Test Data Collection PC

## Slide 68
Cell Gravity Pin

## Slide 69
Cincinnati Test Systems Leak Test Instrumentation

## Slide 70
BET Heater & ACEC Header Plug

## Slide 71
BET / BEV LV Header Plug

## Slide 72
BET / BEV DCFC Header Plug

## Slide 73
BET / BEV HV Header Plug

## Slide 74
BET / BEV HV Header Plug

## Slide 75
Hood Assembly

## Slide 76
BET Vacuum Connector

## Slide 77
BEV3 Vacuum Connector

## Slide 78
Unico Drive Removal Cart

## Slide 79
Cover Leak Solenoid Valve

## Slide 80
Operating
Instructions

## Slide 81
Operator Interface Devices

## Slide 82
Interface Device Table – Manual Stations

## Slide 83
Barcode Reader

## Slide 84
Bypass/Release Toggle Switch

## Slide 85
Cycle Start Button

## Slide 86
Label Printer

## Slide 87
Controls and Indicators

## Slide 88
Operator Console Human Machine Interface (HMI)

## Slide 89
Operator Emergency Stop (E-Stop)

## Slide 90
Operator Push Button Box
Button | Description
RESPONDER CALL | Call a Team Lead.
MAINTENANCE CALL | Call Maintenance Personnel.
PRINT LABEL | Reprint a label if the original printed label is damaged.
RETEST | NOT USED.

## Slide 91
Cell Power Distribution Panel

## Slide 92
SICK Safety Laser Scanner

## Slide 93
Stack Light
Indicator | Action | Description
Horn | Multiple Beeps | Notification Alert
Horn | One Beep | Scan Passed
Blue | Flashing | Operator Load Prompt
Blue | Fast Flashing | N/A
Blue | Solid | In Cycle
White | Flashing | Flexnet Gate Check Query in Progress
White | Fast Flashing | Flexnet Gate Check Failed
White | Solid | Flexnet Gate Check Passed
Red | Flashing | N/A
Red | Fast Flashing | Maintenance Call
Red | Solid | Station Faulted
Yellow | Flashing | Over Cycle
Yellow | Fast Flashing | Responder Call
Yellow | Solid | Approaching End of Cycle
Green | Flashing | Ready for Cycle
Green | Fast Flashing | N/A
Green | Solid | Process Complete

## Slide 94
Status Beacon
Indicator | Action | Description
Red | Flashing | Maintenance (High Priority Fault) Alarm Present
Red | Solid | Non-Maintenance (Low Priority Fault) Alarm Present

## Slide 95
EP680 Bauer Leak Test Data Collection PC

## Slide 96
Cincinnati Test Systems Leak Test Instrumentation

## Slide 97
HMI Screens

## Slide 98
HMI Screen Navigation Paths

## Slide 99
Screen Header

## Slide 100
Select Screen

## Slide 101
Mode Screen

## Slide 102
Scroll List Screen

## Slide 103
DAQ Interlock Screen

## Slide 104
Station Overview Screen

## Slide 105
Cell Overview Screen

## Slide 106
Cell Power and I/O Screen

## Slide 107
Barcode Screen

## Slide 108
EtherNet Public Screen

## Slide 109
Switch Ports and Devices Screen

## Slide 110
Switch Status Screen

## Slide 111
EtherNet Private Screen

## Slide 112
Linear Network Screen

## Slide 113
Device Details Screen

## Slide 114
Alarm Screen

## Slide 115
Maintenance History Screen

## Slide 116
Cycle Time Screen

## Slide 117
Station Throughput Screen

## Slide 118
Configuration Screen

## Slide 119
Signature Screen

## Slide 120
Style Overview Screen

## Slide 121
Style Overview Edit Data Screen

## Slide 122
Quality Screen

## Slide 123
Common Operating Procedures

## Slide 124
Starting Cell in Manual Mode

## Slide 125
Starting Cell in Automatic Mode

## Slide 126
Shutting Down

## Slide 127
Recovering from an Emergency Stop

## Slide 128
Recovering from a Fault

## Slide 129
Mastering Sequence for Pack Coolant Leak Test

## Slide 130
Mastering Sequence for Pack Cover Leak Test

## Slide 131
Auto Mode

## Slide 132
Manual Mode

## Slide 133
Hands On
(At the Machine)

## Slide 134
HMI Screens

## Slide 135
HMI Screen Navigation Paths

## Slide 136
Screen Header

## Slide 137
Select Screen

## Slide 138
Mode Screen

## Slide 139
Scroll List Screen

## Slide 140
DAQ Interlock Screen

## Slide 141
Station Overview Screen

## Slide 142
Cell Overview Screen

## Slide 143
Cell Power and I/O Screen

## Slide 144
Barcode Screen

## Slide 145
EtherNet Public Screen

## Slide 146
Switch Ports and Devices Screen

## Slide 147
Switch Status Screen

## Slide 148
EtherNet Private Screen

## Slide 149
Linear Network Screen

## Slide 150
Device Details Screen

## Slide 151
Alarm Screen

## Slide 152
Maintenance History Screen

## Slide 153
Cycle Time Screen

## Slide 154
Station Throughput Screen

## Slide 155
Configuration Screen

## Slide 156
Signature Screen

## Slide 157
Style Overview Screen

## Slide 158
Style Overview Edit Data Screen

## Slide 159
Quality Screen

## Slide 160
Common Operating Procedures

## Slide 161
Starting Cell in Manual Mode

## Slide 162
Starting Cell in Automatic Mode

## Slide 163
Shutting Down

## Slide 164
Recovering from an Emergency Stop

## Slide 165
Recovering from a Fault

## Slide 166
Mastering Sequence for Pack Coolant Leak Test

## Slide 167
Mastering Sequence for Pack Cover Leak Test

## Slide 168
Modes of Operation

## Slide 169
Manual Station
Operation

## Slide 170
Automated Station
Operation – Auto Mode

## Slide 171
Automated Station
Operation – Manual Mode

## Slide 172
Entering Manual Mode

## Slide 173
Tryout Mode

## Slide 174
Runout Mode

## Slide 175
End of Cycle Hold Mode

## Slide 176
Class Wrap-Up
Closing Remarks
Complete Course Evaluations